## Slide 1: Ki67 Quantification in Neural Stem Cells Cultured inside Porous Collagen Scaffolds
November 2015

## Slide 2: Task
Quantify % of Ki67+ cells in fluorescent images of NSC@scaffolds
Study NSC proliferation
  2D VS 3D
  Collagen VS collagen-GAG scaffolds
Cells stained with
  DAPI (nucleus marker): utilized to identify nuclei
  Ki67 ab: utilized to quantify cell cycle phase
  Nestin ab: NSC marker

## Slide 3: Sample Data
Z-stacks , confocal microscopy
3-channel data
  Red channel: Ki67
  Green channel: nestin
  Blue channel: DAPI

## Slide 4: Algorithm Steps
Identify nuclei per plane
Identify unique nuclei (each nuclei is sectioned in multiple planes)
For each unique nucleus
  Calculate nucleus volume (in voxels)
  Calculate mean Ki67  used for Ki67 segmentation
  Calculate mean DAPI  used for signal normalization

## Slide 5: 4 Patterns of Nucleus Staining Were Observed
1) Smooth nuclei, without any Ki67
2) Smooth nuclei, weak Ki67 foci
3) Smooth nuclei, bright spots of Ki67 and background
4) Irregular nuclei, super-bright irregular Ki67
Red channel: Ki67
Green channel: nestin
Blue channel: DAPI

## Slide 6: 4 Patterns of Nucleus Staining Were Observed
 | Ki67 staining | DAPI staining | Suggested Cell cycle Interpretation1
1 | Not detectable | Elliptic shape | Resting cells G0
2 | Dim foci | Elliptic shape | Interphase G1, S
3 | Bright spots Background all over nucleus | Elliptic shape | Interphase G2
4 | Very bright, multi-bulb | Multi-bulb shape | Prophase-Metaphase
1: based on fig 3 of Du Manoir et al. 1991

## Slide 7: What is considered a Ki67+ cell here
A single Ki67 intensity per nucleus threshold was chosen to distinguish cells that proliferate (stain pattern 2-4) from ones who do not (stain pattern 1)
Ki67 negative
Ki67 positive
 | Ki67 | DAPI
1 | Not detectable | Elliptic shape
2 | Dim foci | Elliptic shape
3 | Bright spots Background all over nucleus | Elliptic shape
4 | Very bright, multi-bulb | Multi-bulb shape

## Slide 8: Results
Chart: day
| 3 | 5 | 7 | 10
C | 44.8188 | 13.1336 | 8.4005
CG | 46.028 | 24.3096 | 12.1778
Sample size (N) 3 2 3 3 3 2

## Slide 9: Comments
Day 5 results coming soon (by Sunday)
Some day 7 and day 10 images need re-processing to improve accuracy
Days 7 and 10 are significantly lower than day 3
CG day 3 and 10 have only n=2.. Other data points have n=3
Data so far do not show that GAG a statistically significant effect
Could try to segment cells into 4 patterns instead of just +/-

## Slide 10: References
du Manoir S, Guillaud P, Camus E, Seigneurin D, Brugal G. Ki-67 labeling in postmitotic cells defines different Ki-67 pathways within the 2c compartment. Cytometry 12(5): 455-63, 1991.
Kill I., Localization of the Ki-67 antigen within the nucleolus, J. Cell Science 109:1253-63, 1996